Holistic power management
Matthew Garrett
<mjg@redhat.com>

---
Holistic
Pronunciation:/həʊˈlɪstɪk, hɒ-/
characterized by the belief that the parts of something are intimately interconnected and explicable only by reference to the whole

---
Computers are complicated
- Lots of parts
- Lots of connections between those parts

---
An example
- Modern CPUs have on-die memory controllers
- Every CPU has its own memory
- Memory takes lots of power to run!

---
CPU C states impact other components
- Package C6 can put RAM into self refresh
- ...but not if a remote CPU is accessing that RAM!
- Can we sensibly migrate RAM when we migrate processes?

---
Not just the CPU
- GPU may be hitting RAM as well
- GPU can operate independently of the CPU
- Power win by ensuring that CPU and GPU work simultaneously rather than entirely independently

---
Considering all the factors
- Processors are devices for turning electricity into heat
- But if they're too good at that, they stop working
- Temperature is tied to performance
- Performance is tied to power consumption
- If a core overheats we get sad

---
Does the scheduler need to care about temperature?
(Spoiler: Probably)

---
Userspace has a role too
- We want to minimise wakeups
- Userspace should be coordinated with the kernel
- Need to consider hardware accesses too

---
How far can we push this?
- External factors influence wakeups
- Can we align our wakeups to AP beacons?
- (Can we align AP beacons to our wakeups?)

---
Power management is a hard problem
And we can make it much harder than we already do. Should we?